## Slide 1: Camera Nano: Pedestrian Detection Team Project Demo
Bharath Ramachandraiah
Nicolas Ojeda Leon
Sameera B Chilmattur
Sandeep Raju
IMSEIT, H-DA
22-July-2019

## Slide 2: Agenda
What
How
What – in much detail
What next?

## Slide 3: Project Goals
Pedestrian Detection Hardware Platform with Future Focus
Single Pedestrian Detection – A step in the door approach
Scalable Thread based Development
Non-Intrusive Feature Addition to Existing Platforms
Common Interfacing

## Slide 4: Prepare Phase Accomplishments
Study of Algorithms
Analysis of Hardware Platforms
Redefining of Goals
Effort Estimation, Expert Review

## Slide 5: Prepare Phase Accomplishments
    Risk Management
      Hardware Platform – cost vs performance vs ease
      ease of development vs future scope
      Features – Usage of Camera Data, Usage of
      LiDAR data, Sensor Fusion
      Hardware Availability – NVIDIA launch
    Risk Mitigation
      Choice of RPI-3 as development vehicle
      VirtualBox Linux for development and trials
      De-scoping Sensor Fusion and Aurix Data Consumption tasks
      Planning “Car” dependency to the end of the project

## Slide 6: Produce Phase Practices – Skinny Sheep Model with Blue Sky Thinking
    Start small
    Every team member had VirtualBox development platform with common goals
    Everyone tried doing things differently in the initial phase
    Technical discussion sessions helped bring ideas together

## Slide 7: Produce Phase Practices – Agile Process

## Slide 8: Produce Phase Practices
    Meetings
      Sprint Planning, Daily Stand-up
      Weekly Status Review Meetings
    Reviews
      Expert Reviews for Interface Design
      2-Eye review and development
    Testing
      Unit Testing
      System Testing

## Slide 9: Budget
    Effort:
      Overall 1000 Hours spent
      About 30% of the time spent in Testing and fine tuning
      About 30% of the time spent in the Prepare phase for Concept, Design and Architecture
      About 25% time spent in Coding and Debugging
      About 5% time spent in Rework due to Change Requests, Reviews and Bugs
    Cost:
      Close to 1000 Euros spent on hardware and consumables – approved by Customer

## Slide 10: Component Interface Design Design Goals and Initial idea
    Design Goals
      Common interface between CameraNano and Maze team projects
      Modular and service-based implementation of features
      New hardware connected to car should be through CAN interface
    Initial idea
      LiDAR detecting obstacle and requests Nano to check if it is pedestrian
        Reduces overall power consumption
        Increases load on PSoC
        Not modular and not scalable

## Slide 11
Gateway
Camera-Nano
AURIX
CAN
CAN
UART
LiDAR
CAN
AntiCollision
UART
Component Interface Design Final design
      Common interface for both CameraNano and MAZE camera's
      More features can be added in AURIX app / Nano in future
      No design impact for camera change and multiple cameras addition

## Slide 12: Component Description: LiDAR
    Functionality
      Acts as additional check for pedestrian detection mechanism
      AURIX can query detection data via CAN and take decisions
    Implementation
      Implemented as separate service and not along with anti-collision
      The detection service is called cyclically by RTOS
      The service provides obstacle distance and angle in relevant ROI
      Send this info to Gateway as response to SDO request

## Slide 13: Component Description: LiDAR
    System Testing
      Simulating AURIX query through PCAN viewer to Gateway
      Gateway sends SDO requesting data to LiDAR
      LiDAR responds to request with latest scan-based detection info
      Gateway forwards results to AURIX (simulated via PCAN viewer)
    Future scope of work
      More robust algorithms to detect human can be run on LiDAR data
      Multiple objects detected and their widths can be sent

## Slide 14: Component Description: Gateway
    Functionality
      Primary interface to AURIX for Camera and LIDAR data retrieval
      Acts as both CANOpen Client and Server
      Periodically recieve and maintain latest camera and LiDAR data
      Supports separate CANOpen indices for Camera and LiDAR data query

## Slide 15: Component Description: Gateway
    Implementation
      Common code framework across student car projects
      Data managed by Gateway -
        LiDAR Data: distance and angle of obstacle
        Camera Data: angle and width of pedestrian detected
    Challenges faced
      CANOpen SDO request for LiDAR data fails after few attempts
        root-cause: SDO dispatcher full due to non-deletion of entries
        solution: periodic call of CANopen_Client_Tick()
    System Testing
      Simulating AURIX query for LiDAR data and Camera data through PCAN and verify through manual inspection and in PCAN

## Slide 16: Component Description: CameraNano Application
    Nvidia Jetson Nano
    Quad Core ARM Cortex A57 at 1.43GHz
    4GB LPDDR4
    128 core Maxwell GPU
    Upto 8 Camera connections
    Latest Linux LTS Distribution - Ubuntu
    OpenCV optimized for the hardware

## Slide 17: Component Description: CameraNano Application
    Functionality
    Detects any Pedestrian in the Camera’s FOV
    Nano obtains camera scans at 30 FPS
    Runs OpenCV-HOG based detection Algorithms
    Filter the false positives
    Compute the angle of location of the Pedestrian from Pixel value
    Delta angle of the Pedestrian
0⁰
Theta
Delta Theta

## Slide 18: Component Description: CameraNano Application
    Interface to the system
    NVidia board is connected to Gateway via UART
    Transmits the detected information
      Theta
      Delta Theta

## Slide 19: Component Description: CameraNano Application
    Implementation
    Single process - 5 threads application
      Detection
      Camera Service
      Communication Tx Service
      Communication Rx Service
      Background
      MailBoxes
      Resources
        Camera
        UART
      Mutex, Semaphore

## Slide 20: Component Description: CameraNano Application
    Challenges faced
    Setting up the gstreamer with relevant configurations for Camera
    Configure camera – Orientations, resolutions, etc.
    Multi-threaded application in C++
    Required power for the board

## Slide 21: Component Description: CameraNano Application
    Unit testing
    Robust Camera and UART testing
    Detection on sample still photos and videos
    Calculations of Theta and Delta Theta for different positions
    Systems Testing
    Subjects at different positions – Verified in the monitor
    Captured positions – Green boxes and Values printed

## Slide 22: Component Description: CameraNano Algorithm
    Feature descriptor (HOG)
      Useful to stand out edges - Shape information
      Normalization to reduce illumination and contrast differences.
      Pixel patches for compact information and noise immunity.
      Single numerical vector output
    Support Vector Machine (SVM)
      Trained decision model
    Non maximum suppression (NMS)
      Merging several overlapping detections

## Slide 23: Pedestrian detection
Starting with the image’s original size, place the window in the top left corner and run the algorithm.
Slide the window (winStride pixels), and run the HOG on the next segment.
For each HOG, make a decision if the window contains a person
Scale the image (by scale factor) and start again
source: Rosebrock. pyimagesearch. [5]

## Slide 24: Feature descriptor (HOG)
Segment the image in patches (64x128)
Calculate the gradient (magnitude and angle)
Divide the patch in 8x8 cells
64
128
source: Mallick. learn OpenCV. [2]
source: Mallick. learn OpenCV. [2]

## Slide 25: Feature descriptor (HOG)
Segment the image in patches (64x128)
Calculate the gradient (magnitude and angle)
Divide the patch in 8x8 cells
Build the histogram for each cell, using 9 angle bins (unsigned 0-180) and the magnitude as the distribution (contributing to 2 bins)
source: Mallick. learn OpenCV. [2]

## Slide 26: Feature descriptor (HOG)
Segment the image in patches (64x128)
Calculate the gradient (magnitude and angle)
Divide the patch in 8x8 cells
Build the histogram for each cell, using 9 angle bins and the magnitude as the distribution
Normalize the histograms in 16x16 blocks (4 contiguous cells)
  Concatenate 4 histograms (36 bins)
  Using L2 norm
  Reduce lighting dependency.
source: Mallick. learn OpenCV. [2]

## Slide 27: Feature descriptor (HOG)
Segment the image in patches (64x128)
Calculate the gradient (magnitude and angle)
Divide the patch in 8x8 cells
Build the histogram for each cell, using 9 angle bins and the magnitude as the distribution
Normalize the histograms in 16x16 blocks
Concatenate 36-bins vectors (histograms) from each block into a 3780 values.
  7 horizontal positions
  15 vertical positions
    7x15x36 = 3780
source: Mallick. learn OpenCV. [2]

## Slide 28: Support Vector Machine (SVM)
    Supervised learning method for classification.
    Closest points determine the hyperplane. (Support vectors)
    Based on the resulting histogram, decide if it is a positive detection.
    Trained with the INRIA person dataset.
    3600 images
source: R. Berwick. MIT. [3]

## Slide 29: Non maximum suppression (NMS)
    Transform many window hypothesis into a single box for each detected pedestrian
    Resulting rectangles are the biggest in the overlapping region

## Slide 30: Component Description: CameraNano Algorithm: Challenges
    Little knowledge about the algorithm.
    Initial research and skinny sheep on Virtual Machine.
    Image quality and mechanical assembly.
    Fine tuning with the final configuration.
    No golden parameters for best results and dependence on camera.
    Fine tuning on real testing scenario.
    Vertical lines false positives.
    Line filtering
    High variability with light conditions.
    Extended testing: different times of the day.

## Slide 31: Component Description: CameraNano Algorithm: Skinny sheep
    Algorithm implementation with actual framework (openCV) on a virtual machine.
    Getting the detection up and running early in the project.
    Risk mitigation.
    Increasing knowledge before hardware arrived.
    GUI for parameter configuration.
    Easier and faster tuning and testing.
    Evaluating behaviour of the algorithm

## Slide 32: Component Description: CameraNano Algorithm: Skinny sheep

## Slide 33: Bibliography
Navneet Dalal, Bill Triggs. Histograms of Oriented Gradients for Human Detection. Cordelia Schmid and Stefano Soatto and Carlo Tomasi. International Conference on Computer Vision
Pattern Recognition (CVPR ’05), Jun 2005, San Diego, United States. IEEE Computer Society, 1, pp.886–893, 2005, <http://ieeexplore.ieee.org/xpls/abs_all.jsp?arnumber=1467360>.
<10.1109/CVPR.2005.177>. <inria-00548512>
Mallick, Satya. “Histogram of oriented gradients”. December 2016. Consulted in: https://www.learnopencv.com/histogram-of-oriented-gradients/
R. Berwick. “An idiot’s guide to Support Vector machines (SVMs)”. MIT. Consulted in: http://web.mit.edu/6.034/wwwbob/svm-notes-long-08.pdf
INRIA Person Dataset. Consulted in: http://pascal.inrialpes.fr/data/human/
Rosebrock, Adrian. HOG detectMultiScale parameters explained. November 2015: pyimagesearch. Consulted in: https://www.pyimagesearch.com/2015/11/16/hog-detectmultiscale-parameters-explained/

## Slide 34: Future Scope of Work
    Future Scope
    Extended features
      Multiple pedestrian detection
      Multiple object detection – such as Animals, Vehicles, etc.
      Multiple cameras for 360 degree field of view
      Quality of camera to improve accuracy
      Camera image stabilisation
      Camera Mounting height, angle
    Algorithms to explore
      Histogram of Oriented Gradients (HOG)
      Scale Invariant Feature Transform (SIFT)
      Convolutional Neural Networks (CNNs)

## Slide 35: Future Scope of Work
    Future Scope cont…
    Libraries
      Tensor flow
      PyTorch
      mlpack
    Speed improvement
      FPGA
      GPUs

## Slide 36: ----ibilities Focus
    Quality
      Review and Testing
        Design and code of every module reviewed in team
        Extensive system tests done regularly for detection and feedback taken up for algorithm fine-tuning
      Algorithm fine-tuning
        Elimination of false positives
        Line detected as human issue – Hough algorithm-based tuning
    Maintainability and Scalability
      LiDAR added as service – helps LiDAR redesign team to easily integrate
      Common code framework for Gateway
      Nano chosen for higher bandwidth – helps integrate multiple cameras

## Slide 37: Lessons Learnt
    Team was risk averse – Needed fewer RPI-3 boards
    Initially lacked imagination in Camera mounting and mechanical designs
    Could have tried benchmarking with 2 different cameras

## Slide 38: Thank you!
    Prof. Dr. Peter Fromm
    Course Director
    IMSEIT, HDA
    Mr. Thomas Barth
    Teaching Fellow
    HDA